## Slide 1: River Pollution Monitoring System ---- AquaSense
John WU
Tommy XIN
Felix FAN

## Slide 2
0. Content
  Motivation
  Current vs AquaSense
  System Description
  Validation
01
04
03
02
  Conclusion
05

## Slide 3
1. Motivation
River Pollution in London
River test samples:
92% samples -> coliform bacteria; 1% samples -> low dissolved oxygen [2].
Impact of Coliform on Residents:
Cause intestinal infection, vomiting, etc [3].
Our Objectives:
Real-time detecting;
Locating contamination
Fig. 1. Levels of E.coli were found around Hammersmith Bridge in west London [1]

## Slide 4: 2. Current vs AquaSense
Fig. 3. ALERT One[4]
Brands | AquaSense | Fluidion ALERT One | ColiMinder | Aquagenx CBT EC+TC Kit
Detection Method | Inorganic sensor + AI model | Automated microbiological analysis | Enzymatic reaction (online) | Colorimetric biochemical reaction
Targets | E. coli + inorganic | E. coli + total coliforms | E. coli, total bacteria | E. coli + coliforms
Response Time | Real-time (seconds) | 2–3 hours | 15–30 minutes | 20–48 hours
Portability | Handheld | Handheld | Station-based | Portable kit
Automation Level | Fully automated | Semi-automated | Fully automated | Manual operation
Estimated Cost | £100–£200 per station | £1,000–£5,000 | £10,000+ | £5–£15 per test
Data Access | Platform + API | WiFi & App | Cloud access | Not supported
Unique Advantages | reagent-free, real-time alerts | ISO-compliant compact form | High accuracy, industrial use | Ultra-low-cost, field-usable
Fig. 2. AquaSense
Fig. 4. Aquagenx Kit

## Slide 5: 3. System Description – Overview

## Slide 6: 3. System Description – Overview
Fig. 5. Flow chart of AquaSense
Fig. 6. Overview of AquaSense
Circuit Design
3D Design
Model Assemble
ML Data Process
Service End
Back-Front End

## Slide 7: 3. System Description – Embedded System
Arduino UNO
Analog Signal
pH sensor
Turbidity sensor
TDS sensor
SCC
SCC
SCC
RTC
EC sensor
Power Supply
DO sensor
SCC
SCC
LORA
Fig. 7. Schematic of Data Transmission
Multi-sensor integrated + LoRa transmission + Power-saving
LORA transmission
TTL Connection
Arduino with sensors
Terminal equipment
MQTT transmission
Webpage
Mobile App

## Slide 8: 3. System Description – Data Processing
Fig. 9. Data Processing procedures
Clustered for distributional similarity; ready for AI modeling.
Unified units, applied long-tail log transform, removed outliers.
Retained measurements with same time and location for contextual relevance.
LLM-assisted filtering of entries mentioning Coliform or E. coli.
Historical water sensor data (2000–2025) from across the UK.

## Slide 9: 3. System Description – AI Model
Fig. 10. Machine Learning Model
E. Coli Concentration output
Neural Network
DO: Dissolved Oxygen
EC: Electric Conductivity
Temp: Temperature
Turb: Turbidity
n/(n+1)
sin(t), cos(t)
Temp * Turb
…
1st: Cond n/(n+1)
2nd: Cond * F(t)
3rd: Turb * Cond
…
StandardScaler
leaky_relu+HuberLoss
L2+Droupout
EarlyStop

## Slide 10: 3. System Description – Data Flow
Fig. 5. Flow chart of AquaSense

## Slide 11: 3. System Description – Dashboard
Details
Fig. 11. Visualized Dashboard
MQTT  Flask  JSON

## Slide 12: 4. Validation
Fig. 10. ML Model Loss
0.83
Fig. 11. Field testing with 88% Accuracy*
*:The 88% of accuracy is based on the previous data, and the lab test of this water sample is on going.

## Slide 13: 5. Conclusion
Advantage
Innovation
Challenge
Strong expansibility and low cost
Inorganic sensors for E.coli detection
Device stability and data accuracy
Notes: 🎯 1. Project Achievements
✅ We have built a fully functional end-to-end system for real-time E.coli monitoring using low-cost IoT sensors and AI models.
Integrated inorganic sensor data with AI-powered analysis
Developed a complete pipeline from data collection → preprocessing → modeling → visualization
Validated model accuracy in lab settings
Delivered live demo-ready platform with automated processing and results display
🔧 2. Current Limitations
⚠️ Real-world deployment is currently limited by infrastructure and scale.
The system currently relies on a single monitoring node; real deployment would require multiple fixed stations along rivers.
Sensor calibration and long-term stability still require field validation
Data standardization across regions needs to be solved for broader compatibility
🚀 3. Future Outlook
🌍 The system is scalable, customizable, and ready for next steps.
Easily adaptable to detect other pollutants (e.g., algae, aromatic hydrocarbons) by retraining the AI model
Potential for integration into city-level water safety platforms
Currently preparing for research paper submission to disseminate our approach
Could serve as a cost-effective alternative to traditional organic detection methods

## Slide 14: Thank you!

## Slide 15: Reference
[1] M. Allen, “Findings of high Thames E.coli levels discovered, as new guidance issued to rowers,” River Action UK, Mar. 27, 2024. https://riveractionuk.com/findings-of-high-thames-e-coli-levels-discovered-as-new-guidance-issued-to-rowers/
[2] “Water Quality Results,” Thames21. https://www.thames21.org.uk/water-quality-results/
[3] “‘Alarmingly high’ levels of E.coli in River Thames found days before Oxbridge Boat Race,” Sky News. https://news.sky.com/story/alarmingly-high-levels-of-e-coli-in-river-thames-found-days-before-oxbridge-boat-race-13102682
[1] M. Allen, “Findings of high Thames E.coli levels discovered, as new guidance issued to rowers,” River Action UK, Mar. 27, 2024. https://riveractionuk.com/findings-of-high-thames-e-coli-levels-discovered-as-new-guidance-issued-to-rowers/
[2] “Water Quality Results,” Thames21. https://www.thames21.org.uk/water-quality-results/
[3] “‘Alarmingly high’ levels of E.coli in River Thames found days before Oxbridge Boat Race,” Sky News. https://news.sky.com/story/alarmingly-high-levels-of-e-coli-in-river-thames-found-days-before-oxbridge-boat-race-13102682
Project Link:
https://github.com/Headmaster218/Thames-pollution-detect-IoT